## Slide 1: System Design AGC/Lidar project
Michael P. Gerlek
29 April 2015

## Slide 2
System Architecture
System Components
Viewer Notes
Implementation Status
Ossim Analyses

## Slide 3: I. System Architecture

## Slide 4: High-level
GeoServer
Ossim
tools
Ingester
tool
SQLite DB
Files on disk
Rialto Viewer
OGC/WPS
HTTP/GET
OGC/WPS
shell process
file I/O
SQL
Other data sources
OGC
Standards
Viewer uses OGC interfaces for data
OGC/WPS used for all backend operations
Allows for alternate frontend with more/less functionality
Allows for new backend algorithms

## Slide 5: Details
point cloud tile DB
WPS
GeoServer
Static File Server
Ossim
tools
Ingester
tool
file
bbox DB
LAS TIF DEM
point cloud tiles
WPS scripts
layers catalog
Cesium
library
point clouds
UI
Rialto Viewer
OGC/WPS
OGC/WPS
HTTP/GET
file I/O
file I/O
shell process
file I/O
SQL
file I/O
SQL
F
L
K
G
C
B
E
D
A
J
I
H
M
N
O

## Slide 6: II. System Components

## Slide 7: A. Files
Files on shared disk
Various geo formats
Both for ingest and as derived products
File DB contains a record for each filename
Written by Ossim tools
Read by Ossim tools

## Slide 8: B. File DB
Single table of a SQLite database
Records the bbox of each file in the system
Read by Ossim to look up needed data sets
Written by Ossim tools as new data files created
Columns
  Filename
  Bounding box
  File type (maybe)
  Associated catalog layer (maybe)

## Slide 9: C. Ossim
Large set of command line tools
  analysis functions (viewshed, HLZ, etc.)
  processing functions (DEM generation)
Inputs can be
  File on shared disk
  Bounding box (File DB used to find files)
Outputs are files on shared disk

## Slide 10: D. Point Cloud Tiles
Raw point data, formatted as tiles
  resolution level, tile column, tile row
“.ria” format
Used for streaming support
Created by PDAL tool
  Already written
Served to client UI as static files
Can be replaced by Point Cloud Tile DB as system matures

## Slide 11: E. Point Cloud Tile DB
Single table of SQLite database
Stores tiles of point clouds
Same structure as tile files, but allows for spatial querying
  Stores each file as a BLOB
Semantically the same as a GeoPackage
  but syntactically different for now
Created by PDAL tool

## Slide 12: F. Layers catalog
Simple text file listing what datasets are available to the UI
  Point clouds, base layer imagery, OSM, etc.
Served by static file server at well-known endpoint
Contents controlled by administrator
  Perhaps updated by ingest process
Already using something very close to this for the UI today
Could be later moved into the database

## Slide 13: G. GeoServer
System has a single GeoServer server
  Can scale out later as needed
Straight open source, no modifications
Provides WPS and static file serving
  Can also be used as TMS, WMS, etc.

## Slide 14: H. Static File Server
GeoServer has the ability to serve static files
Will use this to serve up
  Layer catalog file
  Point cloud tiles

## Slide 15: I. WPS
GeoServer has OGC/WPS support
WPS jobs are created by the UI
  Using standard OGC calls
WPS scripts invoke Ossim command(s)
System already working for viewshed analysis

## Slide 16: J. WPS scripts
Each analysis/processing function has a WPS script
Script just executes Ossim command line tools
Written in Groovy, mostly boilerplate code
System already working for viewshed analysis

## Slide 17: K. Ingester Tool
Command-line tool run to add new data into system
  Typically LAS
Just invokes a WPS process to do the work
  Generate point cloud tiles
  Generate DEMs
  Other needed up-front processing

## Slide 18: L. Rialto Viewer
Viewer for point cloud data
Built on Cesium
Supports running analysis functions
  Viewshed, etc.
  Works with WPS server on backend
Consists of Cesium, point cloud extensions to Cesium, and actual UI

## Slide 19: M. Cesium Library
Geo browser tool
  3D, cross-platform, WebGL, etc.
All JavaScript

## Slide 20: N. Point Clouds in Cesium
Cesium itself does not support point cloud data
We have written a Cesium extension for this
  Uses a simple tiling scheme (static files)
  Supports streaming / progressive rendering
  All JavaScript
Already written, but needs polishing and tuning

## Slide 21: O. Rialto UI
User interface for lidar data
Viewing, processing, measuring, etc.
Built on top of Cesium
Dart and JavaScript

## Slide 22: III. Viewer Notes

## Slide 23: Major UI Pieces
WPS job submission, tracking
Point Cloud as proper Cesium data source
Layer management system
Per-algorithm support
  parameter setting, bbox selection, etc.
Viewer features
  Measurement, mouse coordinates, etc.

## Slide 24: IV. Implementation Status

## Slide 25: Today
We have an end-to-end system that:
  Cesium-based viewer
  Display of streaming point cloud data
  Invocation of WPS jobs
  Viewshed analysis on backend
But:
  More analysis algorithm work needed
  UI needs to be matured

## Slide 26: Done
Viewer support for various data sources
Streaming point cloud support in Cesium
WPS job submission system
Initial analysis algorithms

## Slide 27: To Be Done
Redesign viewer frontend for usability
Production-level UI features for measurement, layer selection, etc.
Production-level point cloud support in Cesium
Production-level WPS job control
Further analysis algorithms
  Already underway
Point cloud tiles in a database
  New code, but building on existing PDAL work

## Slide 28: V. Ossim Analyses

## Slide 29: (tbd)

## Slide 30: Additional Notes